## Slide 1
Verify PCR Products by Gel Electrophoresis (Vertical by PAGE and Horizontal with an Agarose Gel)

## Slide 2: Vertical Gel Electrophoresis
DNA sample
cathode
anode
the porous gel is made of crosslinked chemical chains of polyacrylamide
DNA fragments with negative charge move to the anode
buffer
gel
buffer

## Slide 3
Horizontal Gel Electrophoresis
the porous gel is made of chemical chains of the polysaccharide agarose crosslinked by H-bridges.
Running the electrophoresis at higher voltages gel temperature is increasing and gel is melting because H-bridges are not stable enough.
To verify small fragments with round about 200 bp the pores should be very small.
We need a high concentration of agarose.
But solubility of agarose in buffer is limited to 3 %  pore size is also limited.

## Slide 4
Model
Gel-Electrophoresis

## Slide 5: Separation of DNA Fragments by PAGE
CH3-(CH2)10-CH2-O-SO2-O- Na+
Sodium-Dodecylsulfate (SDS)
+
-
DNA mixture
migration direction
electrophoresis
porous gel
load DNA fragments mixture onto gel
negatively charged DNA fragments migrate to the anode
DNA fragments are separated by their size by the filtration principle of the gel
 small fragments migrate faster than large fragments through the pores

## Slide 6: Length Determination of DNA Fragments by Calibration Curve
DNA marker
sample
1000 bp
700 bp
500 bp
200 bp
100 bp
- DNA fragment lengths of the marker are known (in bp).
- Migration distance of fragments (in cm) can be measured.

## Slide 7: Determination of DNA Fragments Length (Bp) by PAGE
migration distance of DNA standard
migration distance
determine length of DNA fragments by calibration curve
stain DNA fragments
migration distance of sample
calibration curve
log bp

## Slide 8
The End